## Slide 1: Development of a Polarized 3He++ Ion Source for the EIC
Matthew Musgrave
in collaboration with
R. Milner, J. Maxwell, A. Zelenski, G. Atoian, E. Beebe, A. Pikin,
S. Kondrashev, D. Raparia, and J. Ritter
CASE Seminar
February 13, 2019

## Slide 2: Why a Polarized 3He Ion Source?

## Slide 3: Source Concept
Identified as high priority R&D for EIC by EICAC review in 2009, Office of Nuclear Physics Community Review in 2017, and the 2018 assessment of the US National Academy of Sciences.
Requirements
Polarized 3He using optical pumping and injection into EBIS at 5 T
Maximum polarization >70%
Intensity 2.5 × 1011 3He++ ions in 20 𝜇s pulse (~4 mA peak current)
Spin-flip in the beam transport line

## Slide 4: History of Polarized 3He Ion Sources
No new operational 3He ion sources were built since 1984. A number of new ideas were proposed and tested (not successfully).
Spin-exchange and metastability-exchange optical pumping techniques for 3He polarization were greatly improved due to laser development and new applications.

## Slide 5: RHIC EBIS
5T solenoid B Field; 1.5 m ion trap
20 keV electrons up to 10 A
5 Hz maximum repetition rate
5 T

## Slide 6: Principle of EBIS Operation
Radial trapping of ions by the space charge of the electron beam
Axial trapping by applied electrostatic potentials at ends of trap
Ion output per pulse is proportional to the trap length and electron current
Ion charge state increases with increasing confinement time
Output current pulse is independent of species or charge state

## Slide 7: Extended EBIS Upgrade
trap length extension
Add a second 5 T superconducting solenoid for trap length extension: 40% increase in Au intensity
Install 3He polarization and injection system into the upstream solenoid
Opportunity for various vacuum and other minor improvements
3He polarization and injection systems

## Slide 8: Extended EBIS Superconducting Solenoids
5.0 Tesla field, about 1.0 Tesla at field minimum in solenoid separation (~30 cm)
Electron beam propagation test currently in progress.

## Slide 9: Polarized 3He Ion Source

## Slide 10: Metastability Exchange Optical Pumping

## Slide 11: RF Discharge at 2 T
RF discharge parameters strongly affect maximum polarization.
RF discharge power needs to be reduced as 3He polarization increases.
Optimization of the 3He cell geometry and placement of RF electrodes should improve polarization.

## Slide 12: High Field MEOP System in EBIS Spare Solenoid
3He polarization measured with low power probe laser
Operated at magnetics fields of 1, 2, 3, and 4 T
Tested sealed cells at 1 mbar: 5cm OD by 5cm long and 3 cm OD by 10 cm long
Tested open cell system connected to 3He purification system

## Slide 13: Optical Probe Polarimetry
Pumping laser
Probe laser, Toptica, diode laser
Detector
Wavemeter
Pumping laser-Keopsys 10 W 1083 nm- fiber laser
3He cell
Notes: This basic design can be used at high or low field by simply modifying the frequency output of the laser and the light detection method.

## Slide 14: Optical Probe Polarimetry

## Slide 15: Optical Probe Polarimetry

## Slide 16: Measuring Optical Pumping

## Slide 17: 3He Resonance Lines at 5.5 Tesla

## Slide 18: T1 Relaxation in Spare EBIS Solenoid of Sealed Cell
T1 Relaxation measured at 2 T.
T1 s
Chart: 
Gauss/cm
Assume dBx=dBy=dBz=5 G/cm (0.5 mT/cm)
D = 1880 cm2/s/mbar
B0 = 2T
T1 s
Notes: Comparison of the T1 relaxation measured by James Maxwell in 2016 with the laser probe polarimeter and the expected T1 relaxation given the field gradients determined from the plotted field map. The 25% discrepancy could be attributed to the large difference in field gradients at different locations in the 2 T solenoid. There are other factors that could lead to the discrepancy but the field gradients is the big one.

## Slide 19: Field Map of Spare EBIS Solenoid
Chart: 
Gauss/cm
In the multi-Tesla regime, field homogeneity needs to be 1-10 ppm to see a clear NMR signal.
The EBIS solenoid was designed for an ion source and has 0.5% homogeneity (the measured homogeneity is 0.01%).

## Slide 20: Open 3He Cell and Gas Purification System
Non-magnetic brass pneumatic remotely controlled Isolation Valve
OPPIS (RHIC’s polarized proton source) was converted into a high field MEOP system for polarizing 3He.

## Slide 21: Open 3He Cell and Gas Purification System
3He cyro-purification and storage system was built from a modified cryo-pump. Pumps everything except helium!

## Slide 22: RGA Spectra in 3He Open Cell
Large contamination by H2, H2O, Hydrocarbons, Argon as seen in RGA
RGA spectra very clean He signal
Before purification with cryo-pump
After purification with cryo-pump

## Slide 23: 3He Open Cell Results
3He pressure can be controlled with the cryo-pump temperature.
Polarizations have been measured >80% at 2 Torr and high pressures have similar results.
Relaxation time of 30 s measured in open cell. Relaxation rate is limited by metal surfaces in pneumatic valve and gas contamination.
Valve construction and open cell design will be optimized to improve relaxation rate and maximum polarization.

## Slide 24: High Speed Pulsed 3He Valve
Pulsed current causes valve to open by Lorentz Force to the conducting plate in high magnetic field.
Valve design has successful long-term operation in OPPIS: B=3 T, I=100 A, L=5 cm, F=15 N, τ=100µs.

## Slide 25: High Speed Pulsed 3He Valve
Test of high speed pulsed valve in a 2.5 T field in the OPPIS solenoid.
B = 2.5 T, I = 12 A, 3He reservoir pressure = 2 Torr
µs
*Actual valve open time will be longer than the electric current pulse width.

## Slide 26: Gas Ionization Cell for Electron Beam Tests in the BNL TestEBIS
46 cm long, 1 cm diameter gas ionization cell
3 cm long, 0.5 cm diameter down stream barrier (blue)
Electron beams of 6 Amps were successfully propagated through the assembly.

## Slide 27: Extended EBIS Parameters
5 T
5 T
Electron Beam
1 mm diameter
10 Amp
10 keV (actual 20-30 keV)
Charge Capacity = ~1012 elementary charges
3He++ Capacity = ~ 2.5x1011 3He++
Maximum EBIS pulse time = 200 ms
Pressure
1x10-6 mbar during gas injection
1x10-10 mbar standard operation

## Slide 28: Initial Model of Gas Injection System
Ideal pumps
Gas Pulse
30 cm long, 1 cm diameter gas ionization cell
0.5 cm constrictions on either end of the ionization cell
~5.8x109 3He molecules injected into 23.6 cm3 volume
1x10-6 mbar pressure when diffused into ionization cell
Notes: This is a simple geometry to model the gas diffusion after gas injection into the EBIS system. The ionization cell is 30 cm long. Gas is pulsed into the system by assigning a desorption parameter to the small circular region labeled “Gas Pulse” at the start of the simulation. This desorption parameter is then set to zero for the remainder of the simulation.

## Slide 29: MolFlow Model of Gas Diffusion (2ms)
Simulation is paused 2 ms after injection when 3He gas is uniformly diffused in ionization region.
mbar
Notes: In this simulation 3He gas is pulsed into the system during the first 0.05 ms. After 2 ms the 3He is equilibrated within the ionization cell with less than a factor of 2 difference in the pressure at the center and ends of the ionization cell.

## Slide 30: Gas Diffusion and Pumping in Ionization Cell
mbar
Simulation is 300 ms long with 1 ms intervals
~ 6.2x109 injected 3He molecules
1x10-6 mbar when diffused in gas cell (23.6 cm3)
Maximum EBIS pulse rate = 200 ms
Notes: The purpose of this simulation was to measure how fast the 3He gas could be pumped out of the gas injection/ionization system. According to Ed the maximum rate the EBIS delivers pulses to the booster ring is once every 200 ms, so we want to be able to achieve ultra-high vacuum in the ionization cell and definitely in the down stream drift tubes 200 ms after gas is injected. This is important for switching between ion species and for achieving high charge states. This is not very important for 3He. This simulation should be redone with injection of heavier gas.

## Slide 31: Electron Beam Ionization of 3He
Electron Beam
1 mm diameter
10 Amp
10 keV
1% probability that 3He is ionized during traverse of electron beam
Treat electron beam as ideal pump with 99% transparency.
no electron beam
10 Amp electron beam
e-beam, 4x gas pulses
Notes: The electron beam in the EBIS acts as an ion pump on the injected gas. When 3He is ionized it is removed from the gas system and quickly moves downstream into the trap region. The probability of 3He capture during a traverse of the e-beam is determined from the electron impact ionization cross section of 3He, the velocity of 3He, the electron beam current, and the radius of the electron beam. The ionization cross section depends on the electron energy, but the electron energy cancels out elsewhere in determining the probability of 3He capture.

## Slide 32: Electron Beam Ionization of 3He
Charge Capacity = ~1012 elementary charges
10 Amp electron beam
6.2x1011 injected 3He atoms
61% ionized by electron beam
39% pumped out
10 Amp e-beam, 4x gas pulses
24.8x1011 injected 3He atoms
61% ionized by electron beam
39% pumped out
Notes: Here is a comparison of injection of one pulse of gas and 4 pulses (4x the total 3He atoms injected). The purpose of this simulation is to see if we can quickly neutralize the electron beam while keeping the pressure in the ionization cell below 1x10^-6 mbar during injection and below 10^-10 mbar after 200 ms. This slide shows the pressure plotted against time; next slide shows ionization rate. Keep in mind that the electron beam pumps on the 3He gas until it is neutralized, so this simulation looses some accuracy after the electron beam is neutralized, which is the case for the 4 pulse simulation. In future simulations, this needs to be taken into account. I also want to point out that the electron beam effectively maintains the same pump rate until it is neutralized. This is because the mfp of the electrons in the 3He+ ions is 10s or 100s of kilometers, and thus the do not reduce the current of the electron beam.

## Slide 33: Electron Beam Ionization of 3He

## Slide 34: 3He++ Spin Rotator and 6 MeV Polarimeter
3He++ spin rotator and polarimeter in the EBIS HEBT line at 6.0 MeV beam energy.

## Slide 35: Feasibility Experiment
Use extended EBIS and extract fully stripped polarized 3He++ ions accelerated to 6 MeV
Measure 3He + 4He  3He + 4He elastic scattering
Analyzing power has been measured to be 100% at 91oCM at ~5.3 MeV
Process yields 2.66 MeV 3He at 53.6olab and 2.64 MeV recoil 4He at 44.5olab
Precision After 1 Minute at 250 Hz count rate

## Slide 36: Thank you for your attention
MIT-BNL Polarized 3He Ion Source Collaboration
M. Musgrave, R. Milner, J. Maxwell, A. Zelenski, G. Atoian, E. Beebe, A. Pikin, S. Kondrashev, D. Raparia, and J. Ritter
This work was supported by DOE Office of Nuclear Physics, R&D for Next Generation Nuclear Physics Accelerator Facilities.

## Slide 37: Depolarization Contributions in the Electron Beam
See MIT Senior Thesis of Charles S. Epstein:
Development of a Polarized Helium-3 Ion Source for RHIC using the Electron Beam Ion Source , June 2013.

## Slide 38: Polarized 3He at RHIC

## Slide 39: Siberian Snakes
Superconducting helical dipoles
4 Tesla, 2.4 m long with 360∘ twist

## Slide 40: MolFlow – Monte Carlo Simulator for High Vacuum
MolFlow is a Monte Carlo simulator of molecular flow of gases that tracks the trajectories of test particles and increments hits, momentum transfer, and reciprocal of orthogonal speed component on each geometric surfaces.
Surface Parameters: sticky factor, opacity, gas desorption, temperature, velocity, wall sojourn time, and specular/diffuse reflection
Gas Parameters: mass, temperature, radioactive decay
Time-Dependent: sticky factor, opacity, gas desorption
Notes: MolFlow simulates one virtual particle at a time, and it is only applicable at high vacuum where the mean free path of the particle is very long compared to the geometer of the system. Sticky factor is used to determine pump rate. Time dependent desorption is used to pulse gas into the system.